## Slide 1: Boolean Algebra

## Slide 2: LO:
Understand why Boolean algebra is used
Understand basic Boolean algebra notation

## Slide 3: Logic Gates Recap

## Slide 4: Logic Gates Recap
Watch the video: http://www.bbc.co.uk/education/guides/zc4bb9q/revision/2

## Slide 5: Venn Diagram
An alternative way of thinking about logic gates is as a Venn diagram.
The blue areas represent cases where the output is 1.

## Slide 6: Venn Diagram
Here’s another Venn diagram showing the binary inputs.

## Slide 7: Boolean Algebra

## Slide 8: Boolean algebra
Many ways of expressing logic
Another way of expressing logic gates is by using Boolean algebra
Boolean algebra published by George Boole around 1854
Boolean algebra is an expression of logic similar to algebra in maths
Can be used to model logic gates as Boolean equations
It is easier to manipulate Boolean equations than circuit diagrams

## Slide 9: Notation used
Logic Gate | Boolean Symbol | Examples of Use
AND | ∙ x * ^ [no gap or symbol] | A ∙ B (common) A x B A * B A ^ B AB (common)
OR | + v | A + B (common) A v B
XOR | + | A + B
NOT | ! ¬ ‘ | A (common) !A ¬A A’

## Slide 10: Examples
This OR gate can be expressed using Boolean algebra notation like this:
Q = A + B
Note that the + symbol means OR in Boolean algebra, not mathematical addition.

## Slide 11: Examples
This AND gate can be expressed using Boolean algebra notation like this:
Q = A . B
Q = AB
It may also be expressed like this:
Q = A * B
Q = A x B
Q = A ^ B

## Slide 12: Exercises

## Slide 13: Exercise
How can this XOR gate be expressed using Boolean algebra?

## Slide 14: Answer
Q = A + B

## Slide 15: Exercise
How can this NOR gate be expressed using Boolean algebra?

## Slide 16: Answer
Q = A + B
Remember that the bar means NOT.

## Slide 17: Exercise
How can this NAND gate be expressed using Boolean algebra?

## Slide 18: Answer
Q = A . B
Q = AB

## Slide 19: Exercise
How can this NOT gate be expressed using Boolean algebra?
Q

## Slide 20: Answer
Q = A
Q

## Slide 21: More Complex Logic Circuits

## Slide 22: More complex logic circuits
More complex logic circuits can be expressed using Boolean algebra.
What is the Boolean algebra expression at each arrow?

## Slide 23: Answer
Remember that the + means OR.
The arrow furthest to the right represents the final Boolean expression for the circuit.
Brackets are used for each separate gate part of the circuit where necessary.

## Slide 24: Summary
Boolean algebra is used to describe logic such as digital logic circuits
It is used because processes similar to “normal” algebra can be used to manipulate it
Remember the notation used – it may crop up in the exam!